# Parts
## Parts List
- Raspberry Pi Zero W
- DHT11 analog temperature & humidity sensor
- Red LED
- 200Ω resistor
- 1KΩ resistor
- 5V passive piezo buzzer
- NPN Transistor
- Breadboard
- Wiring
## Wiring

## Notes
- LEDs are polarity-sensitive, electricity can only flow through them in one direction. The current flows from the negative (cathode) side to the positive (anode) side. If you wire the LED backwards it will simply not light up. The negative, cathode, pin will be the shorter pin on the LED and also the pin nearest the flat edge of the outer casing.
- The piezo buzzer is also polarity-sensitive. A small plus (+) symbol is engraved in the plastic over the positive pin.
- The NPN Transistor has three pins, known as the base, collector, and emitter pins. The pins can be determined by noticing the flat end of the outer casing and referencing the datasheet for the component:
- Resistors are color coded to identify their value. Each color represents a digit, multiplier, and tolerance. The resistors used use the colors red, black, brown, and gold.
Color	Digit	Multiplier	Tolerance (%)
Black	0	10^0 (1)
Brown	1	10^1 (10)	1
Red	2	10^2 (100)	2
Gold		10^-1 (0.1)	5

The first two colors indicate the value, multiplied by the third color multiplier, and the resistor has a tolerance indicated by the fourth color. The two resistors used are:
Red	Black	Brown	Gold
2	0	10	5

20 * 10 (200) with a 5% tolerance
Brown	Black	Red	Gold
1	0	100	5

10 * 100 (1000) with a 5% tolerance
# Circuits
## Basics
Electricity is the flow of electrons through a conductor, free electrons flow from one atom to the next. There are three primary parameters to keep in mind with electricity: pressure, current, and resistance. Electricity flowing through wires is similar to a closed system of water pipes with a pump pushing the water. If the pump creates a difference in pressure between two points in the pipes, then water will flow from one point to the other. This flowing water is able to do work (such as turning a waterwheel).
Electric pressure, or electric potential difference, is measured in volts. The actual flow of electric charge is known as electric current and is measured in amps. Anything that resists the flow of the electric current provides resistance, which is measured in ohms.
The relationship between the potential difference (volts), current (amps), and resistance (ohms) is a well known mathematical equation knows as Ohm's law.

Where I is current (amps), V is potential difference (volts), and R is resistance (ohms). This means that if you increase the resistance in a circuit, while keeping the same voltage, it will lower the current. If you increase only the voltage, it will increase the current. Etc.
Each of the major functions of the weather station consists of a separate circuit, connected to different pins of the Raspberry Pi.
## Buzzer Circuit
The buzzer circuit is a simple one-transistor audio amplifier. The Raspberry Pi provides 5 volts of electricity and 1.5 amps of current to the buzzer. Sound volume is controlled primarily by current. The 1.5 amps from the Pi directly is not enough to make the buzzer very loud. Because of this, we add a transistor. A transistor consists of a collector and emitter. The flow of electricity through these is controlled by the base. When electric current is applied to the base (at a higher voltage then the emitter), it allows current to flow through the collector and emitter. The actual current through the transistor is a ratio of the currents between the collector and emitter, and to the base.

To ensure that the voltage (or specifically the electric potential difference) to the base of the transistor is higher, we put a resistor there. The transistor amplifies the signal passing through the collector to the emitter (in our case per the transistor's data sheet by a factor of at least 60) and makes the buzzer louder.
## DHT11 Sensor Circuit
The DHT11 sensor circuit is very simple, as most of the components are packaged together into a small module. The power, ground, and data pins merely need to be connected to the appropriate pins on the Raspberry Pi.
## LED Circuit
The LED circuit consists of a light-emitting diode and a resistor. A diode is a component that only allows electric current in one direction. LEDs also emit light when current flows through the diode. LEDs can only handle a small number of amps, so a resistor is used to limit the current.

# Setup
## Install Raspbian
Note: We use NOOBS to install the operating system onto the Pi. The kit we are using came with NOOBS preinstalled on an SD card, but if needed it can be downloaded and copied to an SD card (see instructions here if you need help).
To install Raspbian, we simply need to boot the Pi to NOOBS and select Raspbian in the list of options. Select the language and keyboard as desired. Then hit the 'i' key or click Install. (Note: to reset the Pi to you can hit the shift key during boot to launch NOOBS again and reinstall Raspbian.)

## Connect to WiFi
In most cases you can use the instructions here to connect to wifi.
If connecting to a network with a setup more complicated than a shared key (such as a corporate network), follow these instructions:
1. Open a terminal and type:
   sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
2. Edit that file, add something like (example for MSCHAP):
network={
 ssid="[ssid]"
 key_mgmt=WPA-EAP
 eap=PEAP
 identity="[domain]\[username]"
 password="[password]"
 phase2="auth=MSCHAPV2"
}
1. CTRL-O, enter to save, CTRL-X to exit
2. Reboot (sudo reboot)
## Update Software
We use the Debian Advanced Package Tool (APT) to update the software on the Pi.
Open a terminal. This can be done via the Raspberry Pi menu or using the shortcut.

1. In the terminal type sudo apt-get update. Note: sudo is a special command that runs the subsequent command as superuser. For more information on sudo (and on any command) you can type "man [command]", such as man sudo.
2. Then type sudo apt-get upgrade. Note: this step may take quite some time, up to an hour or more depending on your Internet connection speed, wifi network, and the number of updates needed.
## Set Up Secure Shell (Optional)
It is possible to set up SSH to allow the Raspberry Pi to be accessed remotely from another computer.
1. Click the Raspberry Pi menu, then Preferences, and then Raspberry Pi Configuration.
2. Select the Interfaces tab.
3. Click the Enabled radio button next to SSH.
4. Open a terminal and type ifconfig. The output will contain the IP address of the Pi (next to inet). Then use an SSH program (such as PuTTY) to connect. The default Raspberry Pi user name is "pi" and the password is "raspberry". Note: to change the default password type sudo passwd pi in the terminal and follow the prompts.

# Learning More
## Computer Science
### Books
Title	Author	ISBN
Code: The Hidden Language of Computer Hardware and Software	Charles Petzold	978-0735611313
Head First Learn to Code: A Learner's Guide to Coding and Computational Thinking	Eric Freeman	978-1491958865

### Websites
- https://www.codecademy.com/catalog/subject/all
- https://www.khanacademy.org/computing
- https://mva.microsoft.com
- https://stackoverflow.com
- https://teachyourselfcs.com
## Electronics
### Books
Title	Author	ISBN
Getting Started in Electronics	Forrest M. Mims III	978-0945053286
Make: Electronics: Learning Through Discovery	Charles Platt	978-1680450262
Understanding Basic Electronics	Walter Banzhaf	978-0872590823

### Websites
- https://www.allaboutcircuits.com/textbook
- https://www.circuitlab.com
- https://www.electronics-tutorials.ws
- http://fritzing.org
- http://www.instructables.com/technology/electronics
## HTML and CSS
### Books
Title	Author	ISBN
Head First HTML5 Programming: Building Web Apps with JavaScript	Eric Freeman and Elisabeth Robson	978-1449390549

### Websites
- https://mva.microsoft.com/en-us/training-courses/html5-css3-fundamentals-development-for-absolute-beginners-14207
- https://www.w3schools.com/html/html5_intro.asp
## Javascript
### Books
Title	Author	ISBN
Head First JavaScript Programming: A Brain-Friendly Guide	Eric Freeman and Elisabeth Robson	978-1449340131
JavaScript: The Definitive Guide	David Flanagan	978-0596805524
JavaScript: The Good Parts, 1st Edition	Douglas Crockford	978-0596517748
JavaScript and jQuery: Interactive Front-End Web Development, 1st Edition	Jon Duckett	978-1118871652

### Websites
- https://www.codecademy.com/learn/learn-javascript
- https://javascript.info
- https://mva.microsoft.com/en-US/training-courses/javascript-fundamentals-for-absolute-beginners-14194
- https://www.w3schools.com/jS/default.asp
## Linux
### Books
Title	Author	ISBN
Learning Raspbian	William Harrington	978-1784392192
Raspberry Pi Assembly Language RASPBIAN Beginners: Hands On Guide, 3rd Edition	Bruce Smith	978-1492135289

### Websites
- https://www.debian.org/doc/manuals/debian-handbook
- https://www.debian.org/doc/manuals/debian-reference
- https://www.raspbian.org
## Python
### Books
Title	Author	ISBN
Head First Python: A Brain-Friendly Guide, 2nd Edition	Paul Barry	978-1491919538
Learning Python, 5th Edition	Mark Lutz	978-1449355739
Python Programming for the Absolute Beginner, 3rd Edition	Michael Dawson	978-1435455009

### Websites
- https://www.learnpython.org
- https://mva.microsoft.com/en-US/training-courses/introduction-to-programming-with-python-8360
- https://www.python.org
## Raspberry Pi
### Books
Title	Author	ISBN
Getting Started with Raspberry Pi (Make: Projects)	Matt Richardson and Shawn Wallace	978-1449344214

### Websites
- https://leanpub.com/pi
- https://www.raspberrypi.org/help
- https://www.raspberrypi.org/magpi
- https://www.raspberrypi.org/resources/learn